## Slide 1
AUTONOMOUS DRONE NAVIGATION
GPS-independent local navigation using onboard sensing, ROS 2 and obstacle avoidance

## Slide 2
Background & Significance
UAV autonomy combines sensing, localization, planning and control.
GNSS/GPS may be unavailable or unreliable in indoor and constrained environments.
IMU gives high-rate motion data but integrated position drifts.
Project goal: demonstrate a controlled, measurable GPS-independent navigation pipeline.

## Slide 3
Problem Statement
Conventional small-drone autonomy often depends on GNSS/GPS for global position. In indoor, urban-obstructed, underground, or otherwise GNSS-denied environments, that position source can be unavailable or unreliable. An IMU provides high-rate motion information but its integrated position estimate accumulates drift. Therefore, a practical autonomous drone needs an onboard state-estimation pipeline that combines IMU data with complementary measurements, together with local obstacle sensing and a navigation/controller stack.

## Slide 4
Existing Approaches
IMU + GNSS/INS — strong global reference but depends on GNSS.
Visual-inertial odometry — improves local estimation but adds perception/computation.
LiDAR/IMU and UWB/VIO — stronger drift constraints but higher hardware complexity.
Map-based and mapless navigation — different trade-offs in computation, path quality and exploration.
Learning-based navigation — promising but adds training and validation complexity.

## Slide 5
Literature Survey
Chang et al. (2023): taxonomy and evaluation of GPS-denied UAV navigation.
Gyagenda et al. (2022): GNSS-independent perception, localization and planning.
Youn et al. (2021): low-cost sensor fusion, SLAM and collision-free indoor flight.
Lu et al. (2022): complete GPS-denied MAV architecture.
Ayala et al. (2024): systematic review of autonomous object-goal navigation.
Lin & Zhan (2022): UWB-aided visual-inertial localization.

## Slide 6
Research / Engineering Gap
The individual technologies are established; the project should not claim them as novel.
Target gap: a compact, student-scale integration of estimation, goal navigation, obstacle safety and PX4 control.
Use complementary sensing to manage inertial drift.
Evaluate the complete pipeline with repeatable metrics and fault/recovery tests.
Design around accessible hardware and simulation-first development.

## Slide 7
Objectives
Integrate a flight controller with a ROS 2 companion-computer stack.
Acquire and process IMU data and complementary aiding measurements for local state estimation.
Estimate attitude and local motion without using GPS as the navigation source.
Generate a route or waypoint trajectory from a start position to a destination.
Detect obstacles within the local flight corridor using onboard range sensing.
Modify or stop planned motion when an obstacle creates an unsafe path.
Evaluate navigation accuracy, obstacle avoidance, completion rate and response time.

## Slide 8
Methodology
1. Sensor acquisition and calibration
2. Local state estimation from IMU + complementary aiding
3. Receive destination / waypoint goal
4. Generate route and local trajectory
5. Continuously monitor obstacle safety zone
6. Send trajectory/setpoints through ROS 2 → PX4
7. Hover/stop/reroute on obstacle or fault
8. Reach goal, land and log results

## Slide 9
Hardware Architecture
Quadrotor frame + motors + ESCs
PX4-compatible flight controller
Raspberry Pi-class companion computer
IMU / flight-controller inertial sensors
Optical-flow or local-motion aid (recommended)
Range sensor / ToF / LiDAR for obstacle detection
Battery, power distribution, regulators and safety hardware

## Slide 10
ROS 2 System Architecture
Sensors → state_estimator → /state/odom
mission_manager → goal → planner
obstacle_monitor → safety constraints
local_planner → local trajectory
trajectory_controller → PX4 setpoints
PX4 ↔ uXRCE-DDS ↔ ROS 2 companion computer
RViz2 / logger → visualization and evaluation

## Slide 11
Evaluation
Navigation success rate — percentage of trials reaching the goal without manual takeover.
Goal error — distance between final estimated position and target.
Path length — actual distance travelled versus planned route.
Obstacle response time — detection to safe stop/avoidance command.
Collision/near-collision rate — trials breaching the safety margin.
Waypoint completion rate — waypoints reached within tolerance.
Recovery success rate — successful return to a safe state after injected faults.
Latency — processing and communication delay in critical navigation paths.

## Slide 12
Future Scope & References
Visual-inertial odometry and 3-D SLAM
UWB/LiDAR fusion
Dynamic-obstacle prediction
Learning-based navigation
Larger outdoor GPS-denied experiments
Key references: Chang et al. 2023; Gyagenda et al. 2022; Youn et al. 2021; Lu et al. 2022; Ayala et al. 2024; Lin & Zhan 2022; PX4/ROS 2 documentation.